## Slide 1
Therac-25 Engineering Ethics Case
ENGR 696 Ethics Oral Report (3–5 minutes)
Joe Le | ENGR696| SFSU | Fall 2026

## Slide 2
What Happened?
Therac-25: a computer-controlled radiation therapy machine from the 1980s.
Six known accidents between 1985–1987, each a massive radiation overdose.
Investigations found failures in software, system design, testing, interface, and organization — not just one bug.

## Slide 3
One Ethics Issue: Public Safety
IEEE Code of Ethics: public safety, health, and welfare come first.
Evidence of a serious malfunction should trigger containment and investigation — not the assumption that “the software can't be at fault.”
Safety-critical claims need evidence and independent protection behind them, not just confidence.

## Slide 4
Causes & Mitigation
Too much reliance on software; too few independent hardware interlocks.
Race conditions, unsafe state transitions, confusing operator feedback.
Weak hazard analysis, integration testing, and incident response.
Fix: independent interlocks, fail-safe defaults, real hazard analysis, fault injection, clear alarms, traceable verification, and fast response to field incidents.

## Slide 5
Lesson for OSBAMS
Battery testing controls hazardous stored energy too.
Keep the hardwired E-stop and normally-off contactor independent of the normal software path.
Use a watchdog, latched faults, redundant sensing, staged low-voltage validation, and documented acceptance criteria.
Never connect the battery while the system is in an unexplained fault state.

## Slide 6
References
Leveson, N. G., & Turner, C. S. (1993). An Investigation of the Therac-25 Accidents. IEEE Computer, 26(7), 18–41. https://www.cse.msu.edu/~cse470/Public/Handouts/Therac/Therac_1.html
IEEE. Code of Ethics (revisions adopted June 2020). https://ieee-cas.org/about/ieee-code-ethics
Ethics Unwrapped, The University of Texas at Austin. Therac-25 case study. https://ethicsunwrapped.utexas.edu/case-study/therac-25